## Slide 1: STM32 CCP

## Slide 2
What is CCP(Capture-Compare-PWM)
CCP Module is used General purpose timer and advanced timer for its CCP configurations.
Each Capture/Compare channel is built around a capture/compare register (including a shadow register), an input stage for capture (with digital filter, multiplexing and prescaler) and an output stage (with comparator and output control).
In capture mode, captures are actually done in the shadow register, which is copied into the preload register.
In compare mode, the content of the preload register is copied into the shadow register which is compared to the counter
It has totally 4 channel

## Slide 3
Capture Mode
In Input capture mode, the Capture/Compare Registers (TIMx_CCRx) are used to latch the value of the counter after a transition detected by the corresponding ICx signal.
When a capture occurs, the corresponding CCXIF flag (TIMx_SR register) is set and an interrupt or a DMA request can be sent if they are enabled. If a capture occurs while the CCxIF flag was already high, then the over-capture flag CCxOF (TIMx_SR register) is set. CCxIF can be cleared by software by writing it to 0 or by reading the captured data stored in the TIMx_CCRx register. CCxOF is leared when written to 0.

## Slide 4
The following example shows how to capture the counter value in TIMx_CCR1 when TI1 input rises. To do this, use the following procedure:
Select the active input: TIMx_CCR1 must be linked to the TI1 input, so write the CC1S bits to 01 in the TIMx_CCMR1 register. As soon as CC1S becomes different from 00, the channel is configured in input and the TIMx_CCR1 register becomes read-only.
Program the needed input filter duration with respect to the signal connected to the timer (by programming the ICxF bits in the TIMx_CCMRx register if the input is one of the TIx inputs). Let’s imagine that, when toggling, the input signal is not stable during at must five internal clock cycles. We must program a filter duration longer than these five clock cycles. We can validate a transition on TI1 when eight consecutive samples with the new level have been detected (sampled at fDTS frequency). Then write IC1F bits to 0011 in the TIMx_CCMR1 register.
Select the edge of the active transition on the TI1 channel by writing the CC1P bit to 0 in the TIMx_CCER register (rising edge in this case).
Program the input prescaler. In our example, we wish the capture to be performed at each valid transition, so the prescaler is disabled (write IC1PS bits to 00 in the TIMx_CCMR1 register).
Enable capture from the counter into the capture register by setting the CC1E bit in the TIMx_CCER register.
Procedure

## Slide 5
Capture Block Diagram

## Slide 6
CCP Registers-each 16bit Register
TIMx_CR1 - Timer Control Register
TIMx_SR -Timer Status Register
TIMx_CCMR1 -Timer Capture/Compare Mode Register
TIMx_CCER -Timer Capture/Compare Enable Register
TIMx_CCR1 -Timer Capture/Compare Register

## Slide 7
Capture Program
#include "stm32f10x.h" // Device header
void gpio_init();
void capture_init();
int main()
{
unsigned short int dummy_read=0;
gpio_init();
capture_init();
while(1)
{
if(TIM2->SR &(1<<1))
{
TIM2->SR &=~(1<<1);//capture flag reset
}
dummy_read=TIM2->CCR1;
}
return 0;
}

## Slide 8
void gpio_init()
{
RCC->APB2ENR =(1<<0); //afio clk enable
RCC->APB2ENR |= (1<<2);//porta clk enable,
GPIOA->CRL =0x00000000;//reset
//pa0
GPIOA->CRL &=~(3<<0);//input
GPIOA->CRL |=(1<<2);//input floating
}
void capture_init()
{
    /* Enabling clock for Timer 2*/
    RCC->APB1ENR = (1<<0);//tim2 clk enable
        TIM2->ARR = 2000; //for 2s
        TIM2->PSC = 7999;
    /* Capture Mode, ENABLE Preload*/
        TIM2->CCMR1 = TIM_CCMR1_CC1S_0 ;
        //TIM2->EGR |= TIM_EGR_UG |TIM_EGR_CC1G ;
        /*CC2E : channel 1 enabled; polarity : active low*/
        TIM2->CCER = 0; // off
    TIM2->CCR1 = 0;
    /* Auto Reload Enable */
    TIM2->CR1 |= TIM_CR1_ARPE;//buffer enable
TIM2->CCER |= TIM_CCER_CC1E;//enable
/* Enable Timer Counter */
    TIM2->CR1 |= TIM_CR1_CEN; //timer on
}

## Slide 9
Compare
This function is used to control an output waveform or indicating when a period of time has elapsed.
When a match is found between the capture/compare register and the counter, the output compare function:
  Assigns the corresponding output pin to a programmable value defined by the output compare mode (OCxM bits in the TIMx_CCMRx register) and the output polarity (CCxP bit in the TIMx_CCER register). The output pin can keep its level (OCXM=000), be set active (OCxM=001), be set inactive (OCxM=010) or can toggle (OCxM=011) on match.
  Sets a flag in the interrupt status register (CCxIF bit in the TIMx_SR register). The TIMx_CCRx registers can be programmed with or without preload registers using the OCxPE bit in the TIMx_CCMRx register.
  In output compare mode, the update event UEV has no effect on ocxref and OCx output. The timing resolution is one count of the counter. Output compare mode can also be used to output a single pulse (in One-pulse mode).

## Slide 10
Procedure
Select the counter clock (internal, external, prescaler).
Write the desired data in the TIMx_ARR and TIMx_CCRx registers.
Select the output mode. For example, the user must write OCxM=011, OCxPE=0, CCxP=0 and CCxE=1 to toggle OCx output pin when CNT matches CCRx, CCRx preload is not used, OCx is enabled and active high.
Enable the counter by setting the CEN bit in the TIMx_CR1 register.

## Slide 11
Compare Block Diagram

## Slide 12
CCP Registers-each 16bit Register
TIMx_CR1 - Timer Control Register
TIMx_SR -Timer Status Register
TIMx_CCMR1 -Timer Capture/Compare Mode Register
TIMx_CCER -Timer Capture/Compare Enable Register
TIMx_CCR1 -Timer Capture/Compare Register

## Slide 13
Compare Program
#include "stm32f10x.h" // Device header
void gpio_init();
void compare_init();
int main()
{
gpio_init();
compare_init();
while(1)
{
if(TIM2->SR &(1<<1))
{
TIM2->SR &=~(1<<1);//compare flag reset
}
}
return 0;
}

## Slide 14
void gpio_init()
{
RCC->APB2ENR =(1<<0); //afio clk enable
RCC->APB2ENR |= (1<<2);//porta clk enable,
GPIOA->CRL =0x00000000;//reset
//pa0
GPIOA->CRL |=(3<<0);//output
GPIOA->CRL |=(2<<2);//afio output
}
void compare_init()
{
    /* Enabling clock for Timer 2*/
    RCC->APB1ENR = (1<<0);//tim2 clk enable
        TIM2->ARR = 2000; //for 2s
        TIM2->PSC = 7999;
    /* Output Compare Mode, ENABLE Preload*/
    //oc1m-toggle ,OC1PE: Output compare 1 preload enable
    TIM2->CCMR1 = TIM_CCMR1_OC1PE |(3<<4);
TIM2->EGR |= TIM_EGR_UG |TIM_EGR_CC1G ;
/*CC2E : channel 1 enabled; polarity : active low*/
TIM2->CCER = 0; //compare off
TIM2->CCR1 = 1000;//compare val
/* Auto Reload Enable */
TIM2->CR1 |= TIM_CR1_ARPE;//buffer enable
TIM2->CCER |= TIM_CCER_CC1E;//compare enable
/* Enable Timer Counter */
TIM2->CR1 |= TIM_CR1_CEN; //timer on
}

## Slide 15
PWM-Pulse width Modulation
Pulse width modulation mode allows generating a signal with a frequency determined by the value of the TIMx_ARR register and a duty cycle determined by the value of the TIMx_CCRx register.
The PWM mode can be selected independently on each channel (one PWM per Ocx output) by writing 110 (PWM mode 1) or ‘111 (PWM mode 2) in the OCxM bits in the TIMx_CCMRx register. The user must enable the corresponding preload register by setting the OCxPE bit in the TIMx_CCMRx register, and eventually the auto-reload preload register by setting the ARPE bit in the TIMx_CR1 register.
As the preload registers are transferred to the shadow registers only when an update event occurs, before starting the counter, the user has to initialize all the registers by setting the UG bit in the TIMx_EGR register.
OCx polarity is software programmable using the CCxP bit in the TIMx_CCER register. It can be programmed as active high or active low. OCx output is enabled by the CCxE bit in the TIMx_CCER register. Refer to the TIMx_CCERx register description for more details.
In PWM mode (1 or 2), TIMx_CNT and TIMx_CCRx are always compared to determine whether TIMx_CCRx≤TIMx_CNT or TIMx_CNT≤TIMx_CCRx (depending on the direction of the counter).

## Slide 16
However, to comply with the ETRF (OCREF can be cleared by an external event through the ETR signal until the next PWM period), the OCREF signal is asserted only:
  When the result of the comparison changes, or When the output compare mode (OCxM bits in TIMx_CCMRx register) switches from the “frozen” configuration (no comparison, OCxM=‘000) to one of the PWM modes (OCxM=‘110 or ‘111).
  This forces the PWM by software while the timer is running.
  The timer is able to generate PWM in edge-aligned mode or center-aligned mode depending on the CMS bits in the TIMx_CR1 register

## Slide 17
PWM Block diagram

## Slide 18
CCP Registers-each 16bit Register
TIMx_CR1 - Timer Control Register
TIMx_SR -Timer Status Register
TIMx_CCMR1 -Timer Capture/Compare Mode Register
TIMx_CCER -Timer Capture/Compare Enable Register
TIMx_CCR1 -Timer Capture/Compare Register

## Slide 19
PWM Calculation
/*******Set timer 3 Period for PWM **************
PWM Frequency = 1000Hz
Timer Clock = 8mhz = 8000000 Hz
Time Period Required = (1/1000Hz) = 0.001 Seconds=1ms
Timer clk Formula = fosc/(pre+1)
Prescalar + 1 = 8000000/1000hz)
Prescalar = 7999
Auto_Reload = 2000
***********************************************/

## Slide 20
PWM Program
#include "stm32f10x.h" // Device header
void gpio_init();
void pwm_init();
int main()
{
gpio_init();
pwm_init();
while(1){}
return 0;
}
void gpio_init()
{
RCC->APB2ENR =(1<<0); //afio clk enable
RCC->APB2ENR |= (1<<2);//porta clk enable,
GPIOA->CRL =0x00000000;//reset
//pa0
GPIOA->CRL |=(3<<0);//output
GPIOA->CRL |=(2<<2);//afio output
}

## Slide 21
void pwm_init()
{
/* Enabling clock for Timer 2*/
RCC->APB1ENR = (1<<0);//tim2 clk enable
    TIM2->ARR = 2000; //for 2s
    TIM2->PSC = 7999;
/* Output PWM Mode, ENABLE Preload,PWM mode:1*/
//oc1m-toggle ,OC1PE: Output PWM, 1 preload enable
    TIM2->CCMR1 = TIM_CCMR1_OC1PE |(6<<4);
    //TIM2->EGR |= TIM_EGR_UG |TIM_EGR_CC1G ;
    /*CC2E : channel 1 enabled; polarity : active low*/
    TIM2->CCER = 0; //pwm cahnnel1 off
TIM2->CCR1 = 1000;//50% duty cycle
    /* Auto Reload Enable */
    TIM2->CR1 |= TIM_CR1_ARPE;//buffer enable
TIM2->CCER |= TIM_CCER_CC1E;//pwm enable
/* Enable Timer Counter */
TIM2->CR1 |= TIM_CR1_CEN; //timer on
}